OPC UA and PLCs for Industrial Control
ROS <-> PLC <-> Device

---
Common challenge
- Need to control a device or IO module
  - Only available with industrial fieldbus
  - No basic tcp/ip interface
- Project usually isn’t to implement a fieldbus protocol
  - Simply talking to a device isn’t the deliverable of any project
    - Basic comms blocks active work

---
Common problems
- Too many industrial networks
  - CANbus, Ethernet/IP (IO, not tags), EtherCAT, Profinet
- Open source libraries are lacking
  - Must be very familiar with the protocol
- Limited hours
  - Charge number for hitting a brick wall with X protocol? Debugging comms?

---
Why use a PLC?
- Designed to be used with PLCs
- A PLC is much more flexible than an Anybus
  - Multiple networks all accessed the same way
- Implement logic and control on the PLC
  - More stable, online changes
  - No deadlocks/async issues
  - No ctrl+c leaving things in a weird state
    - Sander pneumatics left spinning
    - Available safety logic and IO

---
Why OPC UA?
- Can’t run ROS in ladder logic or structured text
- OPC UA is easy to use and supported by nearly all vendors
  - Even Rockwell supports it
  - Easy Python libraries in freeopcua
  - Existing ros packages
- Working on a new ros package to automatically map data, create services, etc

---
Create and map IO
Refer to docs, datasheets, esi files, etc

---
Create and map IO
Refer to docs, datasheets, esi files, etc

---
Write PLC code like normal

---
OPC UA mapping
Define a structure to make PC<->PLC comms easier.
The mapped data must have the following structure:
{
   status {
       input {
        Heartbeat: BOOL;
       }
       output {
        Heartbeat	: BOOL;
        Error	: BOOL;
        Connected	: BOOL;
       }
   }
   input {
       data from ros->plc
   }
   output {
       data from plc->ros
   }
}

---
Call FB with OPC UA vars
- Declare in a GVL, expose to OPC UA
- Call in a PRG

---
Access from ROS
Topics and Services created automatically

---
Performance with Beckhoff
- Writing a value takes between 2-3 ms.
  - Quick responses to inputs on PLC
    - Lifting force device
- Manually reading also takes 2-3 ms.
- Subscription publishing time limited by the PLC
  - 50ms minimum on Beckhoff
  - Limits update rate of topics

---
Example: DOUT connected to DIN

---
Example: DOUT connected to DIN
with Timer():
   await node_do.write_value(ua.DataValue(ua.Variant(Value=set_val)))
with Timer():
   di_val = await node_di.read_value()
   read_cnt = 0
   while di_val != set_val:
       read_cnt += 1
       di_val = await node_di.read_value()
[INFO] [1629917936.354802]: DO0 is wired to DI0. Going to set DO0 = True and poll until DI0 is True. DI0 has a 3ms debounce time.
Elapsed time: 0.0021 seconds
Elapsed time: 0.0048 seconds
[INFO] [1629917936.362727]: loop cnt: 1